Propellers: Momentum theory for thrust and power

Use momentum theory to determine the thrust, power requirement and thrust loading coefficient for a 4.2 m diameter propeller that is driving a ship at 20 kn in sea water. Assume that the ideal efficiency of the propeller is 88%, and ignore the effect of the ship wake and the propeller boss.

Solution

m/s

m/s

m2

m3/s

kN

MW

Propellers: Momentum theory for changing propeller arrangements

- A 2.5 m diameter screw propeller is required to produce a thrust of 700 kN at a speed of 24 kn in sea water. Use momentum theory to estimate the minimum power which must be supplied to the propeller.

- Use momentum theory to estimate the power requirement for the situation of item a), if the single 2.5 m diameter propeller is replaced by two 1.5 m diameter propellers.

- Use momentum theory to estimate the propeller diameter of a twin-screw option that delivers the same thrust and absorbs the same power as in the situation of item a).

Solution

- m/s

m2

MW

- m/s (as before)

m2         (for a single propeller)

(for both propellers)

(for both propellers)

MW

- m/s (as before)

(as before)

m2

m

Propeller: Open-water efficiency

Consider a propeller with 4.5 m diameter and the following open-water characteristics:

| J | KT | KQ | (0 | J | KT | KQ | (0 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 0.650 | 0.2573 | 0.0438 |  | 0.820 | 0.1646 | 0.0316 |  |
| 0.680 | 0.2415 | 0.0418 |  | 0.833 | 0.1594 | 0.0309 |  |
| 0.700 | 0.2284 | 0.0401 |  | 0.880 | 0.1380 | 0.0285 |  |
| 0.730 | 0.2119 | 0.0379 |  | 0.920 | 0.1128 | 0.0244 |  |
| 0.760 | 0.1972 | 0.0360 |  | 0.980 | 0.0807 | 0.0198 |  |
| 0.790 | 0.1800 | 0.0336 |  | 1.030 | 0.0421 | 0.0143 |  |

Assume sea water density to be ( = 1026 kg/m3. The inflow velocity is VA = 11.245 m/s.

- Compute the corresponding open-water efficiencies.

- What should be the propeller rpm for the propeller to be at maximum efficiency at ship design speed?

- What should then be the power delivered at the propeller ?

- What is the open-water efficiency?

- What is the averaged axial velocity in the propeller downstream wake ?

Solution

- The open-water efficiency is:

| J | KT | KQ | (0 | J | KT | KQ | (0 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 0.650 | 0.2573 | 0.0438 | 0.608 | 0.820 | 0.1646 | 0.0316 | 0.680 |
| 0.680 | 0.2415 | 0.0418 | 0.625 | 0.833 | 0.1594 | 0.0309 | 0.684 |
| 0.700 | 0.2284 | 0.0401 | 0.635 | 0.880 | 0.1380 | 0.0285 | 0.678 |
| 0.730 | 0.2119 | 0.0379 | 0.650 | 0.920 | 0.1128 | 0.0244 | 0.677 |
| 0.760 | 0.1972 | 0.0360 | 0.663 | 0.980 | 0.0807 | 0.0198 | 0.636 |
| 0.790 | 0.1800 | 0.0336 | 0.674 | 1.030 | 0.0421 | 0.0143 | 0.483 |

- The maximum efficiency is reached for J0 = 0.833. This yields:

Hz	  (or 180 rpm)

The power delivered at the propeller is expressed by the torque:

MNm

MW

- The thrust loading coefficient is:

The axial velocity in the propeller slipstream is:

m/s

Propellers: Propeller curve

Consider a propeller with 4.5 m diameter and the following open-water characteristics:

| J | KT | KQ | (0 |
| --- | --- | --- | --- |
| 0.650 | 0.2573 | 0.0438 | 0.6080 |
| 0.680 | 0.2415 | 0.0418 | 0.6250 |
| 0.700 | 0.2284 | 0.0401 | 0.6350 |
| 0.730 | 0.2119 | 0.0379 | 0.6500 |
| 0.760 | 0.1972 | 0.0360 | 0.6630 |
| 0.790 | 0.1800 | 0.0336 | 0.6740 |
| 0.820 | 0.1646 | 0.0316 | 0.6800 |
| 0.833 | 0.1594 | 0.0309 | 0.6810 |
| 0.880 | 0.1380 | 0.0285 | 0.6780 |
| 0.920 | 0.1128 | 0.0244 | 0.6770 |
| 0.980 | 0.0807 | 0.0198 | 0.6360 |
| 1.030 | 0.0421 | 0.0143 | 0.4830 |

Assume sea water density to be ( = 1026 kg/m3.

The inflow velocity at design speed is VA = 11.245 m/s.

- What should be the propeller rpm for the propeller to be at maximum efficiency at ship design speed?

- What should then be the power delivered at the propeller ?

- What is the open-water efficiency?

- What is the averaged axial velocity in the propeller downstream wake ?

Solution

- The maximum efficiency is reached for J0 = 0.833. The associated rpm is:

Hz	(= 180 rpm)

- The power delivered at the propeller is expressed by the torque:

MNm

MW

- The open-water efficiency is:

- The thrust loading coefficient is:

The axial velocity in the propeller slipstream is:

m/s