Flash Folder:

FlashSide: Shows the Calc Dial, Sensor Eye (adjustment window), and hot-shoe with red manual-fire button.

Hot-Shoe: Shows the flash hot-shoe connection, with the lock, and small metal electrical connection at the very bottom.  When the flash is mounted on the camera body’s hot-shoe, the flash will fire when the shutter button is depressed.

AutoBlue:  In the Auto Mode, this shows the sensor eye set to Blue.

AutoPurple:  In the Auto Mode, this shows the sensor eye set to Purple.

AutoRed:  In the Auto mode, this shows the sensor eye set to Red.

CalcDial:  This shows the Manual Vari-Power (black triangle at bottom) set to Full.  The ISO is set to 400 (White triangle low right).  The outer ring is F-Stops, second ring is distances in feet, inner ring is distances in meters.  This shows F-22 is good for 10’, F-16 is good for 15’, 11 & 20’, 8 & 30’.  It also shows the Auto (colors) Mode ranges.  Purple Mode is a square and a thin line running to the right.  F-22 is opposite the 10’ distance, and the purple line runs to about the 2’ distance.  So, in the Auto Mode, F-22 can be used between 2’-10’.  F-16 is good for 2’-15’; F-8 is good for 5’-30’.

Diffuser1:  With the Flash head set to Wide Angle, the flash throw is appropriate for a 35mm lens.  If you want to use a 28mm lens, the diffuser needs to be inserted into the slot, as shown.

Diffuser2:  This shows the diffuser totally covering the flash head.

ManualFireButton:  Operating the flash manually requires this red button to be pushed to fire the flash.

PcCordConnection:  To operate the flash off-camera, it has to be connected to the camera body with a pc cord.  Then, when the shutter button is depressed, the flash will fire.

FullFull:  In the Full Power Manual Flash Mode, the Vari-Power setting has to be set to Full, and the sensor eye setting also has to be set to M.  Both have to be set.

HalfHalf:  For Half Power Manual Flash Mode, the Vari-Power setting has to be set to ½, and the sensor eye also has to set to ½.  Both have to be set.

ISOSetting400:  The white triangle is set for 400 ISO film.  The 27 is the German equivalent (DIN rating).  It is critical to let the flash know what film is loaded in the camera for the Calc Dial to be effective.

QuarterQuarter:  For Quarter Power Manual Flash Mode, the Vari-Power has to be set to ¼, and the sensor eye also has to be set to ¼.  Both have to be set.

SensorEye1:  A view of the sensor eye: the small round opening under “vari-power”.

SensorEye2:  Another view of the sensor eye.

SixteenSixteen:  For 1/16th Power Manual Flash Mode, the Vari-Power has to be set to 1/16, and the sensor eye also has to be set to 1/16.  Both have to be set.

VariPower:  Manual Flash can be fired at Full Power, or ½ , ¼ , or 1/16th power.  Here it is set to Full Power (black triangle).

ZoomNorm:  With a 50mm lens, the Flash Head should be set to “Norm.”

ZoomTele:  With an 80mm lens, the Flash Head should be set to “Tele.”

ZoomWide:  With a 35mm lens, the Flash Head should be set to “Wide.”  With a 28mm lens, the Flash Head should be set to “Wide” and the Diffuser should be used at the same time.