## Slide 1: ECE408 Fall 2016 Applied Parallel Programming Lecture 16 Atomic Operations and Histogramming

## Slide 2: Objective
To understand atomic operations
  Read-modify-write in parallel computation
  Use of atomic operations in CUDA
  Why atomic operations reduce memory system throughput
  How to avoid atomic operations in some parallel algorithms
Histogramming as an example application of atomic operations
  Basic histogram algorithm
  Privatization

## Slide 3: A Common Collaboration Pattern
Multiple bank tellers count the total amount of cash in the safe
Each grab a pile and count
Have a central display of the running total
Whenever someone finishes counting a pile, add the subtotal of the pile to the running total
A bad outcome
  Some of the piles were not accounted for

## Slide 4: A Common Parallel Coordination Pattern
Multiple customer service agents serving customers
Each customer gets a number
A central display shows the number of the next customer who will be served
When an agent becomes available, he/she calls the number and he/she adds 1 to the display
Bad outcomes
  Multiple customers get the same number
  Multiple agents serve the same number

## Slide 5: A Common Arbitration Pattern
Multiple customers booking air tickets
Each
  Brings up a flight seat map
  Decides on a seat
  Update the the seat map, mark the seat as taken
A bad outcome
  Multiple passengers ended up booking the same seat

## Slide 6: Atomic Operations
If Mem[x] was initially 0, what would the value of Mem[x] be after threads 1 and 2 have completed?
  What does each thread get in their Old variable?
The answer may vary due to data races. To avoid data races, you should use atomic operations
thread1:
thread2:
Old  Mem[x]
New  Old + 1
Mem[x]  New
Old  Mem[x]
New  Old + 1
Mem[x]  New

## Slide 7: Timing Scenario #1
Time | Thread 1 | Thread 2
1 | (0) Old  Mem[x] | 
2 | (1) New  Old + 1 | 
3 | (1) Mem[x]  New | 
4 |  | (1) Old  Mem[x]
5 |  | (2) New  Old + 1
6 |  | (2) Mem[x]  New
Thread 1 Old = 0
Thread 2 Old = 1
Mem[x] = 2 after the sequence

## Slide 8: Timing Scenario #2
Time | Thread 1 | Thread 2
1 |  | (0) Old  Mem[x]
2 |  | (1) New  Old + 1
3 |  | (1) Mem[x]  New
4 | (1) Old  Mem[x] | 
5 | (2) New  Old + 1 | 
6 | (2) Mem[x]  New | 
Thread 1 Old = 1
Thread 2 Old = 0
Mem[x] = 2 after the sequence

## Slide 9: Timing Scenario #3
Time | Thread 1 | Thread 2
1 | (0) Old  Mem[x] | 
2 | (1) New  Old + 1 | 
3 |  | (0) Old  Mem[x]
4 | (1) Mem[x]  New | 
5 |  | (1) New  Old + 1
6 |  | (1) Mem[x]  New
Thread 1 Old = 0
Thread 2 Old = 0
Mem[x] = 1 after the sequence

## Slide 10: Timing Scenario #4
Time | Thread 1 | Thread 2
1 |  | (0) Old  Mem[x]
2 |  | (1) New  Old + 1
3 | (0) Old  Mem[x] | 
4 |  | (1) Mem[x]  New
5 | (1) New  Old + 1 | 
6 | (1) Mem[x]  New | 
Thread 1 Old = 0
Thread 2 Old = 0
Mem[x] = 1 after the sequence

## Slide 11: Atomic Operations – To Ensure Good Outcomes
thread1:
thread2:
Old  Mem[x]
New  Old + 1
Mem[x]  New
Old  Mem[x]
New  Old + 1
Mem[x]  New
thread1:
thread2:
Old  Mem[x]
New  Old + 1
Mem[x]  New
Old  Mem[x]
New  Old + 1
Mem[x]  New
Or

## Slide 12: Without Atomic Operations
thread1:
thread2:
Old  Mem[x]
New  Old + 1
Mem[x]  New
Old  Mem[x]
New  Old + 1
Mem[x]  New
Both threads receive 0
Mem[x] becomes 1
Mem[x] initialized to 0

## Slide 13: Atomic Operations in General
Performed by a single ISA instruction on a memory location address
  Read the old value, calculate a new value, and write the new value to the location
The hardware ensures that no other threads can access the location until the atomic operation is complete
  Any other threads that access the location will typically be held in a queue until its turn
  All threads perform the atomic operation serially

## Slide 14: Atomic Operations in CUDA
Function calls that are translated into single instructions (a.k.a. intrinsics)
  Atomic add, sub, inc, dec, min, max, exch (exchange), CAS (compare and swap)
  Read CUDA C programming Guide 4.0 for details
Atomic Add
  int atomicAdd(int* address, int val);
  reads the 32-bit word old pointed to by address in global or shared memory, computes (old + val), and stores the result back to memory at the same address. The function returns old.

## Slide 15: More Atomic Adds in CUDA
Unsigned 32-bit integer atomic add
  unsigned int atomicAdd(unsigned int* address, unsigned int val);
Unsigned 64-bit integer atomic add
  unsigned long long int atomicAdd(unsigned long long int* address, unsigned long long int val);
Single-precision floating-point atomic add (capability > 2.0)
  float atomicAdd(float* address, float val);

## Slide 16: Histogramming
A method for extracting notable features and patterns from large data sets
  Feature extraction for object recognition in images
  Fraud detection in credit card transactions
  Correlating heavenly object movements in astrophysics
  …
Basic histograms - for each element in the data set, use the value to identify a “bin” to increment

## Slide 17: A Histogram Example
In sentence “Programming Massively Parallel Processors” build a histogram of frequencies of each letter
A(4), C(1), E(1), G(1), …
How do you do this in parallel?

## Slide 18: Any More Questions