## Slide 1: ECE408 Applied Parallel Programming Lecture 16 - Floating Point Considerations Part 2

## Slide 2: Objective
Learn more about CUDA GPU Floating-point Cause of errors
  Deviations from IEEE-754
Understand numerical stability in linear system solver algorithms.
Notes: fdfsdf

## Slide 3: Deviations from IEEE-754
Addition and Multiplication are IEEE 754 compliant
  Maximum 0.5 ulp (units in the least place) error
Division is non-compliant (2 ulp)
Not all rounding modes are supported
No mechanism to detect floating-point exceptions
Notes: The error is measured in ulp (units in the last place), that is the values of the results are multiplied by a power of the base such that an error in the last significant place is an error of 1.

## Slide 4: GPU Floating Point Features
 | Fermi | SSE | IBM Altivec | Cell SPE
Precision | IEEE 754 | IEEE 754 | IEEE 754 | IEEE 754
Rounding modes for FADD and FMUL | Round to nearest and round to zero | All 4 IEEE, round to nearest, zero, inf, -inf | Round to nearest only | Round to zero/truncate only
Denormal handling | Supported | Supported, 1000’s of cycles | Supported, 1000’s of cycles | Flush to zero
NaN support | Yes | Yes | Yes | No
Overflow and Infinity support | Yes, only clamps to max norm | Yes | Yes | No, infinity
Flags | No | Yes | Yes | Some
Square root | Software only | Hardware | Software only | Software only
Division | Software only | Hardware | Software only | Software only
Reciprocal estimate accuracy | 24 bit | 12 bit | 12 bit | 12 bit
Reciprocal sqrt estimate accuracy | 23 bit | 12 bit | 12 bit | 12 bit
log2(x) and 2^x estimates accuracy | 23 bit | No | 12 bit | No

## Slide 5: Numerical Stability
Some order of floating-point operations may cause some applications to fail
Linear system solvers may require different ordering of floating-point operations for different input values
An algorithm that can always find an appropriate operation order and thus a solution to the problem is a numerically stable algorithm
  An algorithm that falls short is numerically unstable

## Slide 6: Gaussian Elimination Example
3X | + 5Y | +2Z | = 19
2X | + 3Y | + Z | = 11
X | + 2Y | + 2Z | = 11
Original
X | + 5/3Y | + 2/3Z | = 19/3
X | + 3/2Y | + 1/2Z | = 11/2
X | + 2Y | + 2Z | = 11
Step 1: divide equation 1 by 3, equation 2 by 2
X | + 5/3Y | +2/3Z | = 19/3
 | - 1/6Y | - 1/6Z | = -5/6
 | 1/3Y | + 4/3Z | = 14/3
Step 2: subtract equation 1 from equation 2 and equation 3

## Slide 7: Gaussian Elimination Example (Cont.)
X | + 5/3Y | +2/3Z | = 19/3
 | - 1/6Y | - 1/6Z | = -5/6
 | 1/3Y | + 4/3Z | = 14/3
X | + 5/3Y | + 2/3Z | = 19/3
 | Y | + Z | = 5
 | Y | + 4Z | = 14
Step 3: divide equation 2 by -1/6 and equation 3 by 1/3
X | + 5/3Y | + 2/3Z | = 19/3
 | Y | + Z | = 5
 |  | + 3Z | = 9
Step 4: subtract equation 2 from equation 3

## Slide 8: Gaussian Elimination Example (Cont.)
X | + 5/3Y | +2/3Z | = 19/3
 | Y | + Z | = 5
 |  | Z | = 3
Step 5: divide equation 3 by 3
We have solution for Z!
X | + 5/3Y | +2/3Z | = 19/3
 | Y |  | = 2
 |  | Z | = 3
Step 6: substitute Z solution into equation 2. Solution for Y!
X |  |  | = 1
 | Y |  | = 2
 |  | Z | = 3
Step 7: substitute Y and Z into equation 1. Solution for X!
X | + 5/3Y | + 2/3Z | = 19/3
 | Y | + Z | = 5
 |  | + 3Z | = 9

## Slide 9
3 | 5 | 2 | 19
2 | 3 | 1 | 11
1 | 2 | 2 | 11
Original
1 | 5/3 | 2/3 | 19/3
1 | 3/2 | 1/2 | 11/2
1 | 2 | 2 | 11
Step 1: divide row 1 by 3, row 2 by 2
1 | 5/3 | 2/3 | 19/3
 | - 1/6 | - 1/6 | -5/6
 | 1/3 | 4/3 | 14/3
Step 2: subtract row 1 from row 2 and row 3
1 | 5/3 | 2/3 | 19/3
 | 1 | 1 | 5
 | 1 | 4 | 14
Step 3: divide row 2 by -1/6 and row 3 by 1/3
1 | 5/3 | 2/3 | 19/3
 | 1 | 1 | 5
 |  | 3 | 9
Step 4: subtract row 2 from row 3
1 | 5/3 | 2/3 | 19/3
 | 1 | 1 | 5
 |  | 1 | 3
Step 5: divide equation 3 by 3
Solution for Z!
1 | 5/3 | 2/3 | 19/3
 | 1 |  | 2
 |  | 1 | 3
Step 6: substitute Z solution into equation 2. Solution for Y!
1 |  |  | 1
 | 1 |  | 2
 |  | 1 | 3
Step 7: substitute Y and Z into equation 1. Solution for X!

## Slide 10: Basic Gaussian Elimination is Easy to Parallelize
Have each thread to perform all calculations for a row
  All divisions in a division step can be done in parallel
  All subtractions in a subtraction step can be done in parallel
  Will need barrier synchronization after each step
However, there is a problem with numerical stability

## Slide 11: Pivoting
 | 5 | 2 | 16
2 | 3 | 1 | 11
1 | 2 | 2 | 11
2 | 3 | 1 | 11
 | 5 | 2 | 16
1 | 2 | 2 | 11
Pivoting: Swap row 1 (Equation 1) with row 2 (Equation 2)
1 | 3/2 | 1/2 | 11/2
 | 5 | 2 | 16
1 | 2 | 2 | 11
Step 1: divide row 1 by 3, no need to divide row 2 or row 3

## Slide 12: Pivoting (Cont.)
1 | 3/2 | 1/2 | 11/2
 | 5 | 2 | 16
 | 1/2 | 3/2 | 11/2
1 | 3/2 | 1/2 | 11/2
 | 5 | 2 | 16
1 | 2 | 2 | 11
Step 2: subtract row 1 from row 3 (column 1 of row 2 is already 0)
1 | 3/2 | 1/2 | 11/2
 | 1 | 2/5 | 16/5
 | 1 | 3 | 11
Step 3: divide row 2 by 5 and row 3 by 1/2

## Slide 13: Pivoting (Cont.)
1 | 3/2 | 1/2 | 11/2
 | 1 | 2/5 | 16/5
 | 1 | 3 | 11
1 | 3/2 | 1/2 | 11/2
 | 1 | 2/5 | 16/5
 |  | 13/5 | 39/5
Step 4: subtract row 2 from row 3
Step 5: divide row 3 by 13/5
Solution for Z!
1 | 5/3 | 2/3 | 19/3
 | 1 | 2/5 | 16/5
 |  | 1 | 3

## Slide 14: Pivoting (Cont.)
Step 6: substitute Z solution into equation 2. Solution for Y!
1 |  |  | 1
 | 1 |  | 2
 |  | 1 | 3
Step 7: substitute Y and Z into equation 1. Solution for X!
1 | 5/3 | 2/3 | 19/3
 | 1 |  | 2
 |  | 1 | 3
1 | 5/3 | 2/3 | 19/3
 | 1 | 2/5 | 16/5
 |  | 1 | 3

## Slide 15
 | 5 | 2 | 16
2 | 3 | 1 | 11
1 | 2 | 2 | 11
Original
1 | 3/2 | 1/2 | 11/2
 | 1 | 2/5 | 16/5
 | 1 | 3 | 11
Step 1: divide row 1 by 3, no need to divide row 2 or row 3
1 | 3/2 | 1/2 | 11/2
 | 5 | 2 | 16
1 | 2 | 2 | 11
Step 2: subtract row 1 from row 3 (column 1 of row 2 is already 0)
1 | 3/2 | 1/2 | 11/2
 | 5 | 2 | 16
 | 1/2 | 3/2 | 11/2
Step 3: divide row 2 by 5 and row 3 by 1/2
Step 4: subtract row 2 from row 3
1 | 3/2 | 1/2 | 11/2
 | 1 | 2/5 | 16/5
 |  | 13/5 | 39/5
Step 5: divide row 3 by 13/5
Solution for Z!
1 | 5/3 | 2/3 | 19/3
 | 1 | 2/5 | 16/5
 |  | 1 | 3
Step 6: substitute Z solution into equation 2. Solution for Y!
1 |  |  | 1
 | 1 |  | 2
 |  | 1 | 3
Step 7: substitute Y and Z into equation 1. Solution for X!
2 | 3 | 1 | 11
 | 5 | 2 | 16
1 | 2 | 2 | 11
Pivoting: Swap row 1 (Equation 1) with row 2 (Equation 2)
1 | 5/3 | 2/3 | 19/3
 | 1 |  | 2
 |  | 1 | 3
Figure 7.11

## Slide 16: Why is Pivoting Hard to Parallelize?
Need to scan through all rows (in fact columns in general) to find the best pivoting candidate
  A major disruption to the parallel computation steps
  Most parallel algorithms avoid full pivoting
  Thus most parallel algorithms have some level of numerical instability

## Slide 17: ANY MORE QUESTIONS? Read Chapter 7