## Slide 1: ECE408/CS483 Applied Parallel Programming Lecture 7: DRAM Bandwidth

## Slide 2: Objective
To understand DRAM bandwidth
  Cause of the DRAM bandwidth problem
  Programming techniques that address the problem: memory coalescing, corner turning,

## Slide 3: Global Memory (DRAM) Bandwidth
Ideal
Reality

## Slide 4: DRAM Bank Organization
Each core array has about 1M bits
Each bit is stored in a tiny capacitor, made of one transistor
Memory Cell
Core Array
Row
Decoder
Sense Amps
Column Latches
Mux
Row
Addr
Column
Addr
Off-chip Data
Wide
Narrow
Pin Interface

## Slide 5: A very small (8x2 bit) DRAM Bank
decode
0
1
1
Sense amps
Mux

## Slide 6: DRAM core arrays are slow.
Reading from a cell in the core array is a very slow process
  DDR: Core speed = ½ interface speed
  DDR2/GDDR3: Core speed = ¼ interface speed
  DDR3/GDDR4: Core speed = ⅛ interface speed
  … likely to be worse in the future
decode
To sense amps
A very small capacitance that stores a data bit
About 1000 cells connected to each vertical line

## Slide 7: DRAM Bursting.
For DDR{2,3} SDRAM cores clocked at 1/N speed of the interface:
  Load (N × interface width) of DRAM bits from the same row at once to an internal buffer, then transfer in N steps at interface speed
  DDR2/GDDR3: buffer width = 4X interface width

## Slide 8: DRAM Bursting
decode
0
1
0
Sense amps
Mux

## Slide 9: DRAM Bursting
decode
0
1
1
Sense amps and buffer
Mux

## Slide 10: DRAM Bursting for the 8x2 Bank
time
Address bits to decoder
Core Array access delay
2 bits
to pin
2 bits
to pin
Non-burst timing
Burst timing
Modern DRAM systems are designed to be always accessed in burst mode. Burst bytes are transferred but discarded when accesses are not to sequential locations.

## Slide 11: Multiple DRAM Banks
decode
Sense amps
Mux
decode
Sense amps
Mux
0
1
1
0
Bank 0
Bank 1

## Slide 12: DRAM Bursting for the 8x2 Bank
time
Address bits to decoder
Core Array access delay
2 bits
to pin
2 bits
to pin
Single-Bank burst timing, dead time on interface
Multi-Bank burst timing, reduced dead time

## Slide 13: First-order Look at the GPU off-chip memory subsystem
nVidia GTX280 GPU:
  Peak global memory bandwidth = 141.7GB/s
Global memory (GDDR3) interface @ 1.1GHz
  (Core speed @ 276Mhz)
  For a typical 64-bit interface, we can sustain only about 17.6 GB/s (Recall DDR - 2 transfers per clock)
  We need a lot more bandwith (141.7 GB/s) – thus 8 memory channels

## Slide 14: Multiple Memory Channels
Divide the memory address space into N parts
  N is number of memory channels
  Assign each portion to a channel
Channel 0
Channel 1
Channel 2
Channel 3
Bank
Bank
Bank
Bank

## Slide 15: Memory Controller Organization of a Many-Core Processor
GTX280: 30 Stream Multiprocessors (SM) connected to 8-channel DRAM controllers through interconnect
  DRAM controllers are interleaved
  Within DRAM controllers (channels), DRAM banks are interleaved for incoming memory requests
Notes: FIXME Channels are also interleaved

## Slide 16: Placing a 2D C array into linear memory space
M0,2
M1,1
M0,1
M0,0
M1,0
M0,3
M1,2
M1,3
M0,2
M0,1
M0,0
M0,3
M1,1
M1,0
M1,2
M1,3
M2,1
M2,0
M2,2
M2,3
M2,1
M2,0
M2,2
M2,3
M3,1
M3,0
M3,2
M3,3
M3,1
M3,0
M3,2
M3,3
M
linearized order in increasing address

## Slide 17: Base Matrix Multiplication Kernel
__global__ void MatrixMulKernel(float* d_M, float* d_N, float* d_P, int Width)
{
// Calculate the row index of the Pd element and M
int Row = blockIdx.y*TILE_WIDTH + threadIdx.y;
// Calculate the column idenx of Pd and N
int Col = blockIdx.x*TILE_WIDTH + threadIdx.x;
float Pvalue = 0;
// each thread computes one element of the block sub-matrix
for (int k = 0; k < Width; ++k)
Pvalue += d_M[Row*Width+k]* d_N[k*Width+Col];
d_P[Row*Width+Col] = Pvalue;
}

## Slide 18: Two Access Patterns
d_M
d_N
W
I
D
T
H
WIDTH
Thread 1
Thread 2
(a)
(b)
d_M[Row*Width+k]
d_N[k*Width+Col]
k is loop counter in the inner product loop of the kernel code

## Slide 19: N accesses are coalesced.
N
T0
T1
T2
T3
Load iteration 0
T0
T1
T2
T3
Load iteration 1
Access direction in Kernel code
…
N0,2
N1,1
N0,1
N0,0
N1,0
N0,3
N1,2
N1,3
N2,1
N2,0
N2,2
N2,3
N3,1
N3,0
N3,2
N3,3
N0,2
N0,1
N0,0
N0,3
N1,1
N1,0
N1,2
N1,3
N2,1
N2,0
N2,2
N2,3
N3,1
N3,0
N3,2
N3,3

## Slide 20: M accesses are not coalesced.
M
T0
T1
T2
T3
Load iteration 0
T0
T1
T2
T3
Load iteration 1
Access direction in Kernel code
…
M0,2
M1,1
M0,1
M0,0
M1,0
M0,3
M1,2
M1,3
M2,1
M2,0
M2,2
M2,3
M3,1
M3,0
M3,2
M3,3
M0,2
M0,1
M0,0
M0,3
M1,1
M1,0
M1,2
M1,3
M2,1
M2,0
M2,2
M2,3
M3,1
M3,0
M3,2
M3,3
d_M[Row*Width+k]

## Slide 21
__global__ void MatrixMulKernel(float* d_M, float* d_N, float* d_P, int Width)
{
1. __shared__float Mds[TILE_WIDTH][TILE_WIDTH];
2. __shared__float Nds[TILE_WIDTH][TILE_WIDTH];
3. int bx = blockIdx.x; int by = blockIdx.y;
4. int tx = threadIdx.x; int ty = threadIdx.y;
// Identify the row and column of the d_P element to work on
5. int Row = by * TILE_WIDTH + ty;
6. int Col = bx * TILE_WIDTH + tx;
7. float Pvalue = 0;
// Loop over the d_M and d_N tiles required to compute the d_P element
8. for (int m = 0; m < Width/TILE_WIDTH; ++m) {
// Coolaborative loading of d_M and d_N tiles into shared memory
9. Mds[tx][ty] = d_M[Row*Width + m*TILE_WIDTH+tx];
Nds[tx][ty] = d_N[(m*TILE_WIDTH+ty)*Width + Col];
__syncthreads();
12. for (int k = 0; k < TILE_WIDTH; ++k)
Pvalue += Mds[tx][k] * Nds[k][ty];
14. __synchthreads();
}
15. d_P[Row*Width+Col] = Pvalue;
}

## Slide 22
d_M
d_N
W
I
D
T
H
WIDTH
d_M
d_N
Original
Access
Pattern
Tiled
Access
Pattern
Copy into
scratchpad
memory
Perform
multiplication
with scratchpad
values
Figure 6.10: Using shared memory to enable coalescing

## Slide 23: Any More Questions? Read Chapter 6